## Slide 1: UVS 1

## Slide 2: Model Parameters
Nominal Wheel Radius (rNominal Dr)
Effective Platform width(bDR)
Number of ticks per 1m (etickDR)
Duty cycle and Speed (dcArray Dr and wArrayDR)

## Slide 3: Phase 1
Experiment for running vehicle in straight line
Series of test carried out to figure best Duty Cycle
1st set of DC -vehicle moves to left.
2nd set of DC-vehicle moves in a straight line.
3rd set of DC- vehicle moves to straight.
4th set of DC-Vehicle move to right.
1st
DC L=30
DC R=30
2nd
DC L=30
DC R=39
3rd
DC L=40
DC R=49
4th
DC L=50
DC R=59

## Slide 4: Phase 1Cont…..
Experiment for 2nd set was setup
Fixed distance (1m, 3m ,5m,7m) and time was calculated for each distance.
Velocity calculated
Used this velocity –calculated time to execute any waypoint in St line.
V for DC 30/39 = 0.6m/s
V for DC 40/49 = 0.68m/s

## Slide 5: Phase 2
No of Experiment | Distance(inch) | time(sec)
1 | 135.25 | 5
2 | 131.75 | 5.02
3 | 133.25 | 5.1
4 | 130.75 | 5.12
5 | 129.75 | 5.07
6 | 133.25 | 5
7 | 131.75 | 5.22
8 | 129.75 | 5.07
9 | 130.75 | 5.12
10 | 133.65 | 4.95
Average | 131.99 | 5.067
Velocity | 26.04894415 | inch/sec
 | 0.661643181 | m/sec

## Slide 6: Experiment for Encoder Count
 | Etick L | Etick R | DC L | DC R | Previous EtickR | Previous EtickL | Distance (inches) | Distance (m) | EtickR dR | EtickL dR
1 | -17755 | -13519 | 70 | 57 | -10818 | -15039 | 98 | 2.4892 | 1085.087578 | 1091.113611
2 | -20238 | -15983 | 70 | 57 | -13519 | -17755 | 89.8 | 2.28092 | 1080.265858 | 1088.59583
3 | -22986 | -18710 | 70 | 57 | -15983 | -20238 | 99 | 2.5146 | 1084.466714 | 1092.817943
4 | -25674 | -21391 | 70 | 57 | -18710 | -22986 | 97 | 2.4638 | 1088.156506 | 1090.997646
5 | -28246 | -23945 | 70 | 57 | -21391 | -25674 | 92.8 | 2.35712 | 1083.525658 | 1091.162096
6 | -30882 | -26567 | 70 | 57 | -23945 | -28246 | 95.2 | 2.41808 | 1084.33137 | 1090.121088
7 | 683 | 398 |  |  | 6 | 279 |  | 0.3736 | 1049.250535 | 1081.37045
8 | 1088 | 796 |  |  | 398 | 683 |  | 0.3736 | 1065.310493 | 1084.047109
9 | 1502 | 1212 |  |  | 796 | 1088 |  | 0.3736 | 1113.490364 | 1108.137045
10 | 1100 | 812 |  |  | 1212 | 1502 |  | 0.3736 | 1070.663812 | 1076.017131
11 | 686 | 411 |  |  | 812 | 1100 |  | 0.3736 | 1073.340471 | 1108.137045
 |  |  |  |  |  |  |  | AVG | 1084.305614 | 1089.454095
 |  |  |  |  |  |  |  | AVG | 1086.879854 | 1086

## Slide 7: Results for Experiment
Chart: DIstances(m)
| 2.4891999999999999 | 2.2809199999999996 | 2.5145999999999997 | 2.4638 | 2.3571199999999997 | 2.4180799999999998 | 0.37359999999999999 | 0.37359999999999999 | 0.37359999999999999 | 0.37359999999999999
Etick R | 1085.0876 | 1080.2659 | 1084.4667 | 1088.1565 | 1083.5257 | 1084.3314 | 1049.2505 | 1065.3105 | 1113.4904 | 1070.6638
Etick L | 1091.1136 | 1088.5958 | 1092.8179 | 1090.9976 | 1091.1621 | 1090.1211 | 1081.3704 | 1084.0471 | 1108.137 | 1076.0171

## Slide 8: Phase 3
Estimation of b
 | etickl | etickR | b
58.55 | 1576.456 | 1091.113611 | 0.436130116
69.54 | 1580.356 | 1088.59583 | 0.372060373
66.6 | 1584.466714 | 1092.817943 | 0.388396655
68.12 | 1588.156506 | 1090.997646 | 0.383985917
65 | 1583.525658 | 1091.162096 | 0.398535764
63.12 | 1584.33137 | 1090.121088 | 0.411945288
69.4 | 1589.250535 | 1081.37045 | 0.385031681
61.45 | 1565.310493 | 1084.047109 | 0.412055472
71.89 | 1567.490364 | 1108.137045 | 0.336180971
59 | 1570.663812 | 1076.017131 | 0.441100795
 |  | Avg | 0.396542303
Etick=1089

## Slide 9: dcArrayDR ,wArrayDR
DC | Distance(inches) | Distance(m) | Time | Translational | Angular
-100 | -426 | -10.8204 | 2 | -5.4102 | -93.359793
-90 | -402 | -10.2108 | 2 | -5.1054 | -88.100086
-80 | -331.5 | -8.4201 | 2 | -4.21005 | -72.649698
-70 | -300 | -7.62 | 2 | -3.81 | -65.746333
-60 | -257 | -6.5278 | 2 | -3.2639 | -56.322692
-50 | -209 | -5.3086 | 2 | -2.6543 | -45.803279
-40 | -155.5 | -3.9497 | 2 | -1.97485 | -34.078516
-35 | -148 | -3.7592 | 3 | -1.253066667 | -21.623238
-34 | -147.5 | -3.7465 | 3 | -1.248833333 | -21.550187
-33 | -137.5 | -3.4925 | 3 | -1.164166667 | -20.089157
0 | 0 | 0 | 0 | 0 | 0
33 | 137.5 | 3.4925 | 3 | 1.164166667 | 20.0891573
34 | 147.5 | 3.7465 | 3 | 1.248833333 | 21.5501869
35 | 148 | 3.7592 | 3 | 1.253066667 | 21.6232384
40 | 155.5 | 3.9497 | 2 | 1.97485 | 34.078516
50 | 209 | 5.3086 | 2 | 2.6543 | 45.8032787
60 | 257 | 6.5278 | 2 | 3.2639 | 56.322692
70 | 300 | 7.62 | 2 | 3.81 | 65.746333
80 | 331.5 | 8.4201 | 2 | 4.21005 | 72.649698
90 | 402 | 10.2108 | 2 | 5.1054 | 88.1000863
100 | 426 | 10.8204 | 2 | 5.4102 | 93.3597929